MATERIAL SAFETY DATA SHEET

MARIL PRODUCTS, INC.				EMERGENCY TELEPHONE

320 West 6th Street				           (800) 424-9300 - CHEMTREC

# Tustin, CA  92780

(714) 544-7711				Poisondex Classifications

Control3@earthlink.net				 	Health:		1

Fire:		0

Reactivity:	0

PRODUCT NAME:					DATE ISSUED:     LAST REVISION:

Control III Laboratory Germicide			April 1, 1999      May 1, 2005

_________________________________________________________________________________

SECTION 1:  IDENTITY

TRADE NAME:			Control III Laboratory Germicide

CHEMICAL FAMILY:		Quaternary ammonium compound

CHEMICAL NAME:		Mixture of alkyl dimethyl benzyl ammonium chloride

and alkyl dimethyl ethyl benzyl ammonium chloride

COMMENTS:	Control III Laboratory Germicide is a ready to use product and should not be diluted before use.

SECTION II:  HAZARDOUS INGREDIENTS/IDENTITY INFORMATION

| Hazardous Component | OSHA-PEL | % |
| --- | --- | --- |
| 1. n-Alkyl (C14-60%; C16-30%; C12-5%; C18-5%) DIMETHYL BENZYL AMMONIUM CHLORIDE (CAS # 68391 - 01-5) | None Established | <1.0% |
| 2. n-Alkyl (C12-68%; C14-32%) DIMETHYL ETHYL BENZYL AMMONIUM CHLORIDE (CAS # 68956-79-6) | None Established | <1.0% |

SECTION III:  PHYSICAL/CHEMICAL CHARACTERISTICS

Boiling Point:			212(F

Vapor Pressure:			N/A

Vapor Density:			N/A

Solubility in Water:		Complete

Appearance and Odor:		Clear Watery Liquid with Sweet Odor

Specific Gravity:			0.9998

Melting Point:			N/A

Evaporation Rate:		N/A

SECTION IV:  FIRE AND EXPLOSION HAZARD DATA

Flash Point:			>212(F Pensky Martins Closed Cup

Flammable Limits:		N/A

Extinguishing Media:		N/A

Special Fire Fighting

Procedures:			None

Unusual Fire and

Explosion Hazards:		None

Control III Laboratory Germicide MSDS Sheet

Page 2 of 2

SECTION V:  REACTIVITY DATA

Stability:			Stable

Incompatibility:			Anionic Materials, Strong Oxidizers

Hazardous Decomposition

(or by-products):		None

Hazardous

Polymerization:		   	Will Not Occur

SECTION VI:  HEALTH HAZARD DATA:

Routes of Entry:

Inhalation:		N/A

Eye Contact:		Red or Tearing Eyes

Skin Contact:		N/A

Ingestion:		N/A

First Aid:

Skin: 			N/A

Eyes:			In case of eye contact, flush eyes with water; call a doctor

Ingestion:		N/A

Chemical Listed as Carcinogen By:

OSHA:				No

I.A.R.C. Monograph:		No

National Toxicology Program:	No

SECTION VII:  PRECAUTIONS FOR SAFE HANDLING AND USE

Spills:			Rinse Spills with Water to Drain

Waste Disposal:		Pour Down Drain/Place Empty Container in trash

Handling/Storing:	No special precautions

# SECTION VIII:  CONTROL MEASURES

Respiratory Protection:			None

Ventilation:

Local Exhaust			N/A

Mechanical (General)		N/A

Protective Gloves:			N/A

Eye Protection:				Goggles or Face Shield

Protective Clothing/Equipment:		None

msdslabg.doc